## Slide 1: Introduce about Research Field: Beam modeling analysis
Doan Manh Hung

## Slide 2: Contents
Introduction
Main purpose
Conclude

## Slide 3: Introduction
Initial-Design Stage Finite Element Modeling of Automobile Body: Beam/Joint
Shell/Plate
Beam
Joint Spring or Joint Rate
Automobile Body Design

## Slide 4
Plate/shell
Accurate Response
Initial Design Purpose
Beam
Joint Spring
Beam
Beam models
1) give more design freedom in initial body configuration,
2) are computationally much more efficient than Shell Models,
3) However, it is very difficult to have Good Beam Models.
Motivation for Beam Modeling ?

## Slide 5: In Auto Bodies, Thin-walled Closed Beams are Used as the Main Load Carrying Members….
B-Pillar
In Comparison with open beams
They Have better Stiffness-to-Mass Ratios than Solid Beams
They Have Higher Torsional Rigidity than Open Beams
But, their structural behavior is not so simple……

## Slide 6
Flexure/Bending
(2 D.O.F X 2 = 4 D.O.F)
Torsion
(1 D.O.F)
Extension
(1 D.O.F)
6 D.O.F
* Usual Deformations: Extension, Bending and Torsion
Investigate deformation patterns:

## Slide 7: Analysis for Straight Box Beams
+
+
Distortion (1 DOF)
Warping(1 DOF)
These three DOF’s are coupled Need New Analysis
x
y
z
Straight Box Beam
=
+
+
Extension (1 DOF)
Flexure/Bending (4 DOF)
Torsion(1 DOF)

## Slide 8
Thin-Walled “Straight” Box Beams and Results
“Curved” Box Beams and Results,
Thin-walled Closed Beams having General Sections (straight case)
Our Higher-Order Beam Theory Will Consider Additional Section Deformations!!

## Slide 9: Verification in a Curved Box Beam, Static (Out of Plane)
Timoshenko beam
Plate element
Present Beam
R=500mm
b=25mm
h=50mm
t=1mm
=90deg
V=1N
Rigidly constrained
Fixed
Present Theory : Torsion + Flexure + Bending +
Warping + Distortion
(3DOF)
(5DOF)

## Slide 10
Thank you for concentration!